## Slide 1: Class 21: Making a Process (Virtual Memory)
cs4414 Fall 2013
University of Virginia
David Evans

## Slide 2: Recap: Last Week
run::Process::new(program, argv, options)
Rust Runtime
spawn_process_os(prog, args, env, dir, in_fd, …)
fork()
libc: fork()
linux kernel: fork syscall
int 0x80
jumps into kernel code
sets supervisor mode

## Slide 3: Plan for This Week
How the Kernel Makes a Process
  Virtual Memory
Thursday: diving into fork.c

## Slide 4: Batch Processing
Program
Computer Center
Your Program Runs
Output: Invalid Operation
Charge: $174.32
From Class 3:

## Slide 5: Process Abstraction
Provide each program with the illusion that it owns the whole machine.
The best example of this way to do things is Linux, which is an operating system, which is a program that keeps track of other programs in a computer and gives each its due in space and time.
Guy Steele, “How to Grow a Language”
HT: Anonymous for posting link in Piazza forum

## Slide 6: Memory Isolation
Memory Space 1
Memory Space 2
Process 1 should only be able to access Memory Space 1
Process 2 should only be able to access Memory Space 2

## Slide 7: Software-Based Memory Isolation
…
movq %rax, -8(%rbp)
…
Original Code
Safe Loader
…
movq -8(%rbp),%rdx
andq %rdx,%rgx
movq %rax, %rdx
…
“Sandboxed” Code
Assumes %rdx is reserved and %rgx is protected and holds a mask for the memory segment

## Slide 8
SOSP 1993
SOSP 1993

## Slide 10: Hardware-Based Memory Isolation
…
movq %rax, -8(%rbp)
…
Original Code
Running Code
…
movq %rax, -8(%rbp)
…
Memory Space 1
Memory Space 2

## Slide 11: Virtual Memory
address in Process P
Virtual Memory Mapping
physical address owned by Process P
User-level processes cannot access physical memory directly: all memory addresses created by process P are virtual addresses, mapped into physical addresses owned by process P

## Slide 12: Getting Into the Details…

## Slide 13
SOSP 1967
Procedure Base Register:
segment number of executing procedure
Argument Pointer
Base Pointer
Linkage Pointer
Stack Pointer
Descriptor Base Register

## Slide 14: Generating an Address
18 bits
18 bits
218 = 262144

## Slide 15
Addressing Mode selects:
Argument Pointer
Base Pointer
Linkage Pointer
Stack Pointer

## Slide 16: Descriptor Base Register
What does MULTICS need to do to switch processes?

## Slide 18: 1982
"It used to be that programs were easy to copy and change. But manufacturers began to lose money as many people made copies of software and gave them to their friends. Now, many manufacturers have figured out how to 'copy-protect' discs. A copy-protected disc–like a cartridge–can’t be copied or changed. To our mind this is a disaster: Most people learn programming by changing programs to fit their own needs. This capability of customization is what makes computers so attractive. New ways of copy protection will probably be found soon. Until then, a computer owner may have to put up with being 'locked out' of his own machine.”
Popular Mechanics, January 1982

## Slide 19
Intel 80186
Intel 80286
First x86 Processor with Virtual Memory Support
“Protected Mode”

## Slide 20
http://en.wikipedia.org/wiki/File:Intel_i80286_arch.svg

## Slide 21: Five x86-64 Processor Modes
Real Mode: pretend to be an 8086
20-bit direct-access address space
Protected Mode: “native state”
System Management Mode: platform-specific power management and security (separate address space)
Compatibility Mode: pretend to be x86-32
IA-32e/64-bit Mode: run applications in 64-bit address space
“For brevity, the 64-bit sub-mode is referred to as 64-bit mode in IA-32 architecture.”

## Slide 22
Protected State (can only be modified by the kernel):
RFLAGS (includes EFLAGS)
Control Registers
Includes I/O Privilege Level
CR0 bit 0: controls if processor is in protected mode
CR3: page directory base register

## Slide 23: Address Translation
Logical Address
Segmentation Unit
Linear Address
Paging
Unit
Physical Address
Memory

## Slide 24: Accessing Memory
16 bits to select segment, 16- 32- or 64- bits to select offset
Actual addressable space for user-level process in Unix:
247 bytes = 128TiB

## Slide 25: Computing the Linear Address
Logical Address
Segmentation Unit
Linear Address
Paging
Unit
Physical Address
Memory
Segment Selector
Offset
Logical (“General”, “Virtual”) Address
Segment selection is inferred from instruction type

## Slide 26: Fetching an Instruction
Code Segment
Instruction Pointer (Offset)
EIP
CS
32 bits
16 bits
Table Index
Ring
Global or Local Table
13 bits
1
2
Only Kernel can write to Segment Registers

## Slide 27: Segmentation Tables
Global Descriptor Table (GDT)
13 bits – up to 8192 entries
Segments can overlap!
base address
limit
linear address space
0-264 - 1

## Slide 28: Segmentation Tables
Global Descriptor Table (GDT)
Local Descriptor Table
(per process)
13 bits – up to 8192 entries
How does the processor find the GDT/LDT?

## Slide 29
The GDT and LDT are just data structures in memory!
Special registers store their locations

## Slide 30
Logical Address
Segmentation Unit
Linear Address
Paging
Unit
Physical Address
Memory

## Slide 31: Paging
264 linear addresses
What would it cost to have 264 bytes of RAM?
Logical Address
Segmentation Unit
Linear Address

## Slide 32
$10 per 1GB = 230 bytes
264 bytes = $10 * 234
$172B ~ ½ Google’s Market Cap

## Slide 33: Paging
Logical Address
Segmentation Unit
Linear Address
Paging
Unit
Physical Address
Memory
We don’t need to store the whole address space in memory!
Most of it is unused, and we can store rarely-used parts on the disk.

## Slide 34
Image from Wikipedia
Linear Address
Paging
Unit
Physical Address
Memory

## Slide 35: Overview (Intel 386)
CR3
Page Directory
Page Table
Physical Memory
Dir
Page
Offset
CR3+Dir
Page Entry
Page + Offset
12 bits
(4K pages)
10 bits
(1K tables)
10 bits
(1K entries)
32-bit linear address

## Slide 36: Page Table Entries
CR3
Page Directory
Page Table
Physical Memory
Page Entry
Page + Offset
20 bits: physical address of page
12 bits: flags
user/kernel page
write permission
present

## Slide 37: 386 Checkup
CR3
Page Directory
Page Table
Physical Memory
Dir
Page
Offset
CR3+Dir
20 bits addr / 12 bits flags
Page + Offset
12 bits
(4K pages)
10 bits
(1K tables)
10 bits
(1K entries)
32-bit linear address
How many pages do we need to store the page table?

## Slide 38: How slow is this???!
Logical Address
Segmentation Unit
Linear Address
Paging
Unit
Physical Address
Memory
GDTR
Global Descriptor Table
CR3
Page Directory
Page Table
Physical Memory
Dir
Page
Offset

## Slide 39
Logical Address
Segmentation Unit
Linear Address
Paging
Unit
Physical Address
Memory
GDTR
Global Descriptor Table
CR3
Page Directory
Page Table
Physical Memory
Dir
Page
Offset
Translation Lookaside Buffer (Cache)

## Slide 40: Page Fault
CR3
Page Directory
Page Table
Physical Memory
Page Entry
20 bits: physical address of page
12 bits: flags
user/kernel page
write permission
present

## Slide 41
How common are page faults?

## Slide 42
top -o mem -stats pid,command,cpu,mem,mregion,vsize,faults

## Slide 43
top -o mem -stats pid,command,cpu,mem,mregion,vsize,faults
Physical Memory:
9106M used (2553M “wired” – cannot be paged out)
+ 5090M unused
= 14196M
where is my missing ~2GB???!
Virtual Memory: 594G (total)

## Slide 44
How expensive is a page fault?

## Slide 45
#include <stdio.h>
#include <stdlib.h>
int main(int argc, char **argv) {
char *s = (char *) malloc (1);
int i = 0;
while (1) {
printf("%d: %x\n", i, s[i]);
i += 4;
}
}
What will this program do?
> ./a.out
0: 0
4: 0
8: 0
12: 0
…1033872: 0
1033876: 0
1033880: 0
1033884: 0
Segmentation fault: 11

## Slide 46: Charge
Make progress on your projects: everyone should have a clear idea what you are doing now
Will post more details on next deliverable (design reviews) soon
Challenge: write a program that takes N as an input and produces (nearly) exactly N page faults.